## Slide 1: Large Board
Summary of Suggested Changes

## Slide 2: Dimensions
46.1 mm x 72.9 mm
4 holes for M3 screws
Vias for testing
Development Region

## Slide 3: Major Components
IMU
  ICM-20948
  SPI
Level Shifters
Antennas
  SMA
  Chip
    2450AT42B100E
USB

## Slide 4: Pin Headers
Teensy
Exterior Voltage sources
  VDDD, VDDIO, VBAT, VIN
Boot Source Select
  Can tie to VDDD
Current measurement
  VDDD, VDDIO, VBAT
VIN Select
  Teensy vs USB
VDDD Select
  1V vs VBAT
VDDIO Select
  1.8V vs VIN vs VBAT
Rx/Tx
  USB vs Teensy
Lighthouse
ADC
  Input and LDO Output

## Slide 5: Changes
No more I2C for IMU
Swapped GPIO12/13 for IMU
Modified scum schematic ALWAYS_ON_LDO
Better labeling
Through-hole antenna
Swap Tx level shifter direction
Lighthouse localization pin headers
Access to ADC pins
External VIN
Current measurement
Changed schematic labels of Teensy header